## Slide 1
What is SWARM?
SWARM Object Manipulation
with Local Mean Control
Shiva Shahrokhi, Mable Wan, Lillian Lin, and Aaron T. Becker
sshahrokhi2@uh.edu mmwan2@uh.edu lklin@uh.edu atbecker@uh.edu .
Problem
Problem
Results
Dr. Becker
Shiva Shahrokhi Mable Wan Lillian Lin
Games
Actual Size
SWARM is 100+ kilo-bots moving an object to a desired location. All robots have the same “brain”, aka program, and respond to the same global inputs, the brightest lights.
Advantages of SWARM:
Can pass through tight structures
Can bend around obstacles
Affordable to replace the robots
Control variables: Mean and Variance
Irrelevant Robots
Robots in front of the object
Blocks object from moving in desired direction
Pushes object further away from the goal when ideal direction is going left.
Solution
Centroid Matching
False goal completion
Robots go in loops trying to follow local goal.
Robots and object get “stuck” in that place
Local Mean Control
Consider only relevant robots
Obstacle Considerations
are Necessary
Obstacles create irrelevant robots that hinder object’s movement
Local Control is
More Effective
Peripheral data induces noise in calculations
Local control demonstrates the ranges of radii that affect the object differently
Mean
Variance
Object’s
Centroid/ Local Goal
Mean
Irrelevant Robots
Mean
Local Goal
Robot Direction
Irrelevant Robots
Relevant Robots
Irrelevant
Robots
Relevant Robots
Method
Calculates the mean of the robots within a certain radius, the relevant robots.
Concept successful in simulation!
Increases probability
of reaching the goal in experiments.
Reduces noise for
calculating desired
direction for robots
Decreases chances of
the block getting stuck
Conclusions
Mean calculations successfully exclude:
Robots that are stuck behind obstacles
Robots that are in front of object
Play games for our research!
Goal
Ideal Direction
Main Problem: Considering all the robots in the mean calculation hinders the object’s ideal movements to the goal.
Direction #1
Direction #2
Swarmcontrol.net
Ideal Direction