## Slide 1
Global inputs: symmetry
Shaping a Particle Swarm With a Shared Control Input Using Boundary Interaction
Shiva Shahrokhi, Aaron T. Becker
sshahrokhi2@uh.edu, atbecker@uh.edu .
Using boundary interaction
Another way to break symmetry is using boundaries:
usually workspaces have boundaries.
If a robot is touching a wall, the other robot can go anywhere in the reachable set while the first robot is immobile.
Δ configuration space shows reachable Δg by moving one robot to touch a wall and then adjusting the second robot.
Best-first search algorithm
Results
Global inputs: All robots get the
same input
Symmetry: control 2 of 2n DOF
Previous work: used a single obstacle
in the middle of the workspace
Constraints: this obstacle is impractical,
especially in 3D
Current work: circular workspace
YouTube channel
Website, C.V.
Department of Electrical and Computer Engineering,
University of Houston
The shortest path when Δg is reachable is when the robot that collides with the wall moves toward the reflection of its goal.
ε is used to ensure particles do not overlap
Sequence of moves to goal position:
An A*-like algorithm considers all potential paths to find the shortest one using best-first search
Distance and number of moves for different goal positions of the blue robot when all the other positions are fixed
Algorithm extends naturally to 3D
Cylindrical workspaces are common in biology
ε= 0.001
ε= 0.05
ε = 0.1
3
4
5
6
5
4
3
2
1
youtu.be/5t1BTPhLod8